## Slide 1: Ethernet Routing Overview

## Slide 2: Agenda
Ethernet history
Frame types
Ethernet transmission
Addressing
Bridging/Switching
Bridge protocols
Switch Functions
Carrier Ethernet

## Slide 3: History
Invented by Robert Metcalfe and David Boggs in ~1972
10Mbps 1985
100Mbps 1995 (802.3u)
1Gbps 1998 (802.3z)
10Gbps 2002 (802.3ae)
40/100Gbps 2010 (802.3ba)

## Slide 4: Standardization
IEEE 802 LAN/MAN Standards Committee
  http://www.ieee802.org
Jointly published as ISO standards
802.2 Logical Link Control (LLC)
802.1 MAC Bridging
802.3
802.4
802.5
802.6
802.9
802.11
802.12
802.1 Mgt.
Physical
layer
Data link
layer
OSI model
Application
Presentation
Application
Session
Transport
Network
Data Link
Physical

## Slide 5: Physical Layer
Responsible for encoding the payload and transmission on the physical media
Preamble
Start frame delimiter
RS (Reconciliation Sublayer)
PCS – Physical Coding Sublayer
  Codes data before Tx
  Decodes data after Rx
  Collision, carrier sense
PMA (Physical Medium Attachment)
  Tx, Rx, Reset, Clock recovery, Link integrity, Align
PMD (Physical Medium Dependent)
  Digital to Physical conversion

## Slide 6: Media Access Control Layer
Media Access Control (MAC)
  Framing
  Addressing
  Error detection
  Collision avoidance (Half duplex)
  Collision handling (Half duplex)
MAC Control
  Pause frames

## Slide 7: Ethernet Frame Format

## Slide 8: MAC Addresses
Address structure
  OUI (vendor) part
  Device part
Ethernet addressing
  Unicast
  Multicast (X1-XX-XX-XX-XX-XX)
  Broadcast (FF-FF-FF-FF-FF-FF)
  Locally/Globally administered
Multicast/Broadcast Source addresses not allowed

## Slide 9: Frame Types
Ethernet II
  EtherType: 1536 – 64K
LLC (Logical Link Control protocol)
  EtherType: 0-1535
LLC/SNAP (Subnetwork Access Protocol)

## Slide 10: Ethernet Frame transmission
Min Frame 64 bytes
  64/(64+20)
  ~76,2% utilization
  = 7,62Gbps (10G)
Max frame 1518 bytes
  1518/(1518+20)
  ~98,7% utilization
  =9.87Gbps (10G)
9600 byte jumbo frame now widely supported
  Again to decrease overhead

## Slide 11: Repeaters
Forwarding based on Layer1 info
Amplification of electrical signal
Extending the diameter of the LAN and the number of attached stations
Only legacy equipment (10/100Mbps)

## Slide 12: Bridging
Forwarding based on Layer2 info
Division of collision and access domains

## Slide 13: Bridging (cont’d)
Bridges can learn MAC addresses on segments
Interconnecting different LAN technologies
  Ethernet, Token-ring, FDDI etc.
Bridging behavior
  Forward all multicast and broadcast frames
  Forward unknown DMAC addresses
  Don’t forward ’local’ frames (when SMAC and DMAC is on the same Ethernet segment)
  Don’t forward frames with bad checksum

## Slide 14: Switching
Defined as Multiport bridging by Kalpana 1990
Multiple access domains, higher network bandwidth utilization
Less ’shared’ network traffic to be snooped
Switching Functionality
  Forward based on Destination MAC Address (DA)
  Learn stations positions in network based on Source MAC Addresses (SA) - “Backward Learning”
  Age of old address entries based on activity timer
© Retro-Computing Society of Rhode Island

## Slide 15: Switching (cont’d)
Flood frames with
  Broadcast DA
  Unknown multicast DA
  Unknown unicast DA
Forward to known port(s):
  Known multicast DA to multiple ports
  Known unicast DA to one port
Never:
  Send frame back to source port

## Slide 16: Bridge Protocol Datagram Units (BPDU)
Group of link-local messages
  MAC address range 01-80-C2-00-00-00 to -0F
MAC Control
  Pause frames 01:80:C2:00:00:01
  Reserved Ethertype 0x8808
  Used for lossless transmission (congestion/backoff signaling)
Slow Protocols
  Link Aggregation Control Protocol (LACP)
  Rapid & Multiple Spanning Tree Protocol (RSTP / MSTP)
  Operations, Administration, and Maintenance (OAM)
MAC control frames must never be forwarded to another Ethernet segment
  i.e. terminated in the switch

## Slide 17: Spanning Tree Protocol (STP)
Used to avoid loops in bridged LANs
LLC encapsulation
  Reserved DSAP
Reserved multicast address
  01:80:C2:00:00:00
Individual ports can be in one of these states
  Listening,Learning, Forwarding or Blocking
Rapid Spanning Tree Protocol (RSTP, 802.1w)
  Enhanced STP with much faster convergence
Multiple Spanning Tree Protocol (MSTP, 802.1s)
  “RSTP per VLAN”
  Same port states as STP
  Up to 64+1 ‘network trees’.
  Mapping of VLANs to trees

## Slide 18: VLAN
Virtual LAN IEEE802.1Q
Separation of broadcast domains
Some security benefits
Insert new VLAN header
  4 bytes after MAC adresses and in front of current Etype field
  Ethertype 0x8100
Changes to Ethernet frame size

## Slide 19: General Switch Function
MAC – validates frame
Classification – CoS selection
Address Engine – destination computation
MAC – transmit frame

## Slide 20: Reception – MAC
Validates the incoming frame
  Detects coding, protocol and Frame Check Sequence errors
Collects statistics information
  Management and monitoring (SNMP, RMON, SMON)

## Slide 21: Classification
Parses frame and assigns Class of Service (CoS) level, based on
  Layer 1 (Port number, speed)
  Layer 2 (SA, DA, VLAN, EtherType, MPLS label)
  Layer 3 (Protocol, IP addresses, DSCP)
  Layer 4 (TCP/UDP Port numbers)
CoS is used to select the queue in the Queue System
Main differentiators:
  Which fields can be used to assign CoS
  Number of Classes
  Programmability, flexibility
    State-machine vs ACL (t-CAM)

## Slide 22: Queue System
Distributed or shared memory subsystems
  Sharing between ingress/egress & ports
  A fully shared memory system gives the best (theoretical) performance
Main differentiators:
  Amount of available memory (granularity, efficiency)
  # Priority queues (Classes of Service)
  Quality of Service
    Scheduling strategy
    Drop strategy
    Queue overflow handling

## Slide 23: QoS – Scheduling Strategies
Strict Priority (SP)
  Always serve the highest priority queue first. Go on to lower priority if no data in the current queue.
Round Robin (RR)
  Always ask the next queue in the sequence
  Go on until finding data in a queue
Weighted Round Robin (WRR)
  As RR, but queues are allowed to send a number of packets corresponding to their individual weights.
Weighted Fair Queuing(WFQ)
  Give low bandwidth traffic high priority
    Monitor incoming flows
    Prepare scheduling

## Slide 24: Queue System – Overflow Handling
Tail-drop
  Drop incoming packets
Head-drop
  Drop the oldest packet (conceptually, ”shift packets”)
  May help TCP discover packet discard earlier
Intentional drop mechanisms
  Drop packets on basis of queue level, packet priority, etc., before or after the queue

## Slide 25: Drop Strategies
Random Early Detection (RED)
  Randomly drops packets in periods of medium load  TCP decreases data rate rather than backing off
Weighted Random Early Detection (WRED)
  As RED, but drops packets selectively based on some marking principle, e.g. IP DSCP
Output queue level
Packet discard probability
0
1
Empty
Treshold
Full
Notes: http://www.qosforum.com/docs/glossary/glossary.htm:
Random Early Detection (RED):
A congestion-avoidance algorithm developed in the early 1990s built on the base-level TCP behavior of automatically slowing transmissions when packet loss is detected. RED tries to anticipate congestion by monitoring a queue on a router When the specified threshold is reached, it randomly discards packets. This is an implicit signal that the originating applications should slow their transmissions before congestion becomes severe. Unlike CBQ, WFQ, SFQ, RED does not require flow-state in routers.
Also a process of intelligent cell discard that occurs within an ATM switch when its buffer capacity is exceeded. RED discards cells in a round-robin fashion among affected connections.

## Slide 26: Scheduling Strategies
Strict Priority (SP)
  Always serve the highest priority queue first. Go on to lower priority if no data in the current queue.
3
3
3
3
3
3
3
3
3
3
3
2
2
2
2
2
2
2
2
2
2
2
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0

## Slide 27: Scheduling Strategies (2)
Round Robin (RR)
  Always ask the next queue in the sequence
  Go on until finding data in a queue
3
3
3
3
3
3
3
3
3
3
3
2
2
2
2
2
2
2
2
2
2
2
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0

## Slide 28: Scheduling Strategies (3)
Weighted Round Robin (WRR)
  As RR, but queues are allowed to send a number of packets corresponding to their individual weights.
  WRR Variants
    Weight unit is bytes rather than packets
    Queue with higher weight is served more frequently
3
1
1
1
Weight
3
3
3
3
3
3
3
3
3
3
3
2
2
2
2
2
2
2
2
2
2
2
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0

## Slide 29: Scheduling Strategies (4)
Weighted Fair Queuing(WFQ)
  Give low bandwidth traffic high priority
    Monitor incoming flows
      Bandwidth of flows or groups of flows
    Prepare scheduling
      High and low priority packets in separate queues
Notes: http://www.qosforum.com/docs/glossary/glossary.htm:
Weighted Fair Queuing (WFQ):
Per-flow packet scheduling in network elements that automatically categorizes traffic flows into high and low priority, based on volume of packets seen by a router or switch. Low-bandwidth traffic has effective priority over high-bandwidth traffic, and high-bandwidth traffic shares the transmission medium proportionally according to assigned weights. Like class-based queuing (CBQ), WFQ is designed to prevent any one traffic type from entirely eclipsing another. By default, WFQ favors lower-volume traffic flows over higher-volume ones (for example, a routine e-mail over a large FTP download).
(unknown source)
Some source indicates this principle…
”Tag any packet with a preferred transmission time.
The packet with the lowest tag value is sent first.”

## Slide 30: Drop Strategies – WRED
Weighted Random Early Detection (WRED)
  As RED, but drops packets selectively based on some marking principle, e.g. IP precedence.
Output queue level
Packet discard probability
0
1
Empty
Treshold 1
Treshold 2
Full
Low precedence packets are discarded using RED1
High precedence packets are discarded using RED2
Notes: http://www.qosforum.com/docs/glossary/glossary.htm:
Weighted Random Early Detection (WRED):
Combines IP precedence and Random Early Detection (RED) capabilities to provide differentiated performance characteristics for different classes of service. Packets with a higher IP precedence are less likely to be dropped than those with lower precedence

## Slide 31: Drop Strategies – summary
Random Early Detection is an extension to a scheduler, NOT a scheduling strategy in itself
RED works on top of a scheduling mechanism to assist TCP in adapting to network congestion

## Slide 32: Addressing Engine – Address Table
Content Addressable Memory, using (VID, MAC) as key
Key is 60 bit  hashing used to avoid using HW CAMs
Learning based on (VID, Source Address)
Main differentiators:
  Capacity (8K – 64K entries)
  Hash depth (2 – 8)
  Learning speed (wire-speed vs not wire-speed)

## Slide 33: Addressing Engine/Analyzer
Looks up Addresses, and computes destination port-set based on
  Destination Address (Port Group ID)
  Source port (masking, for avoiding loops)
  VLAN Spanning Tree state (learn/forward)
  VLAN Id
  Mirroring and CPU copy/redirect operations
  Port Aggregation
Computes port bitmask:
  DEST = (pgid AND src AND stp AND vlan OR mirror OR cpid) AND aggr

## Slide 34: Addressing Engine - Example
DEST = (pgid & src & stp & vlan | mirror | cpid) & aggr
Destination: ports 6 & 7
Source: port 0
STP: all ports active
VLAN: ports 2 & 1 not member
Mirroring: port 3
Copy to CPU signaled
Aggregation: ports 7 & 6
Send frame to:
  CPU queues (CPU copy)
  Port 6 (ordinary forward)
  Port 3 (mirror copy)

## Slide 35: Transmission – MAC
Transmits the outgoing frame
  Detects collision and retries transmission, formats frame according to the standard and generates Frame Check Sequence
  Performs updates to the frame
    VLAN insertion, User_priority / DSCP rewrite
Collects statistics information
  Management and monitoring (SNMP, RMON, SMON)

## Slide 36: Carrier Ethernet - Challenges
Ethernet originally designed for data communication within a LAN
  Providing high bandwidth at low cost
  “Best effort” technology: If dropping data, just retransmit
Why use Ethernet in telecom and other time sensitive applications?
  It’s dirt cheap! (compared to other legacy technologies)
What’s the challenge?
  Replacing deterministic technologies with “best effort”
  Delivery of telecom services, spanning multiple networks
  Requirement for delivery guarantee, beyond what standard Ethernet is capable off
  A new set of attributes on top of Standard Ethernet is required
iiiiiiii

## Slide 37: Carrier Ethernet - Definition
Definition of Carrier Ethernet (by MEF):
“A ubiquitous, standardized, carrier class Service and Network defined by 5 attributes, that distinguish it from familiar LAN based Ethernet

## Slide 38: Carrier Ethernet – Definition, cont’d
Standardized services
Service: A common way of handling a flow of frames
Service concept defined in MEF 6.1 (Service types) and MEF 10.1 (Service properties)
Services provided to multiple customers instead of only one customer (LAN)
Services provided on multiple networks instead of on one (LAN) network
LAN A
LAN B
LAN A
LAN C
LAN B
LAN A
LAN B
LAN C
CPE
CPE
CPE
CPE
CPE
E-Line
E-Tree
E-LAN

## Slide 39: Carrier Ethernet – Definition, cont’d
Scalability
Need to be able to scale to millions of nodes as opposed to a few hundreds or thousands
Large number of services to be supported as opposed to a few services
Use of double VLAN tagging where an outer Service tag (S tag) is used for carrying the Customer tagged (C tagged) traffic.

## Slide 40: Carrier Ethernet – Definition, cont’d
Reliability
Link failure protection switching within 50ms
Fault recovery as fast as possible to ensure uptime according to Service License Agreement (SLA). “Five nines” (99.999%) uptime equals total max downtime of only 5.26 min/year!
Services provided on multiple networks instead of on one (local) network
G.8031
Line protection switching
G.8032
Ring protection switching
Active path
Backup path
RPL Owner
RPL (Ring Protection Link)
1+1: Both links active
1:1: One active, one backup

## Slide 41: Carrier Ethernet – Definition, cont’d
Service Management
Must be able to quickly provision bandwidth for specific service across the network
Must be able to monitor and detect faults across multiple networks and on equipment from multiple vendors
Features supporting service management include
  OAM (Operations, Administration, and Maintenance)
    Link OAM (link discovery, link monitoring, remote failure indication, loopback)
    ITU-T Y.1731 Performance Monitoring and Fault Management
  SAT (Service Activation Test) – ITU.T Y.1564 - Ensuring bandwidth profile parameters:
    CIR and EIR (Committed and Excess/Peak Information Rate)
    CBS and EBS (Committed and Excess/peak Burst Size)
  RFC2544 (measuring e.g. throughput, latency, and frame loss)

## Slide 42: Carrier Ethernet – Definition, cont’d
Quality of Service (QoS)
QoS required to support multiple different services (time sensitive applications, e.g. voice and video as well as standard data services)
QoS required to treat traffic from multiple customers traffic in accordance with each individual SLA
Bandwidth profile parameters (CIR/EIR, CBS/EBS) are used in “color coding” the service frames:
  Green: Frame is CIR/CBS compliant and must be forwarded in the network
  Yellow: Frame is not CIR/CBS compliant but EIR/EBS compliant and might be forwarded in the.
  Red: Frame neither CIR/CBS nor EIR/EBS compliant´. Frame must be dropped.

## Slide 43: Carrier Ethernet – Timing/synchronization
To ensure the reliability and quality as well as enabling the service management, synchronization of across the network is also needed
Timing synchronization across the network using PTP – Precision Timing Protocol – IEEE1588 (-2008 aka PTPv2):
  Agreement throughout the network of both clock phase and frequency
  Clock phase and frequency communicated using standard Ethernet frames
  Minimizes latency and delay variations across the network
  Provides accuracy in the nanosecond range
  Important also within Industrial Ethernet (Indstrial Automation, Time-Sensitive Networking/TSN), another big focus area of Microsemi ENT BU

## Slide 44: Thank You
Nov 2017

## Slide 45: Carrier Ethernet Acronym List
Acronym list © Copyright 2010 Fujitsu Network Communications