## Slide 1
CE AMS SerDes IP
FAE Training 2022
© 2022 Marvell confidential. All rights reserved.
1

## Slide 2: Legal Statement:
CONFIDENTIAL INFORMATION
  The information contained in this presentation is the confidential and proprietary information of Marvell. You are not permitted to disseminate or use any of the information provided to you in this presentation outside of Marvell.
This material MUST NOT be distributed to customers

## Slide 3: Training Outline
5 | 5nm 112G COMPHY IBIS-AMI Model
6 | 5nm 112G COMPHY MCESD/API
7 | 5nm 112G COMPHY AE Guidelines
1 | 5nm 112G COMPHY Architecture
2 | 5nm 112G COMPHY Function
3 | 5nm 112G COMPHY DSP Training
4 | 5nm 112G COMPHY Firmware

## Slide 4
Time | Topic | Presenter
8:00 – 8:15 | Get to know the team | All
8:15 – 8:35 | Introduction | Mike Sorna
8:35 – 09:35 | Architecture - RX | Fang Dong
9:35 – 10:05 | Architecture - RX Q&A section | 
10:05 – 10:20 | Break | 
10:20 – 10:50 | Architecture - PLL | Eugene Kim
10:50 – 11:00 | Architecture – PLL Q&A section | 
11:00 – 11:15 | Break | 
11:15 – 11:35 | IBIS-AMI Model | Evelina Zhang
11:35 – 11:50 | IBIS-AMI model Q&A section | 
11:50 – 12:30 | Lunch | 
AGENDA

## Slide 5: 5 nm COMPHY_112G_ADC Introduction
Ever-increasing demand of higher I/O bandwidth for infrastructure
PAM-4 signaling has been adopted for higher bandwidth efficiency
Carrier
Enterprise
Automotive
Data Center
Supercomputer
Storage
High Def. video conference
5G
SerDes

## Slide 6: 5 nm 112G SerDes
Key Features:
Configurable bus widths with PAM2 and PAM4 modulation:
  PAM2: 32-/40-bit for ≤ 32 Gbps and 64-/80-bit for > 32 Gbps
  PAM4: 64-/80-bit for ≤ 56.25 Gbps and 128-/160-bit for > 56.25 Gbps
Tx: 6 tap equalization, 2 post-taps, and 3 pre-taps
Rx:
  Supports > 40 dB loss at 112 Gbps with optimized firmware-based training
  6 pre-taps, 16 post-taps and 8 floating taps
1-tap Decision Feedback Equalization (DFE) or 1+D mode to support long reach and reduce burst error and Forward Error Correction (FEC) performance
Programmable Analog-to-Digital Converter (ADC) resolution to support lower data rates with better power efficiency
Least Mean Square (LMS) adaptation to maintain optimum performance with different operating duty cycles to optimize power
Real-time Eye Opening Measurement (EOM) monitor
Real-time PRBS-pattern FEC error histogram with post-FEC BER
Real-time SNR at digital slicer averaged or by PAM4 symbol level
Real-time Single Bit Response (SBR) estimation at ADC input
Built-in temperature/process monitor with advanced compensation schemes
Test Chip Status:
R1.0 included in STC05-R3, silicon arrived in March 2022
R1.1 included in ASIC BU SoC, tapeout targeted for December 2022
Application | Next-generation solution focused on 800G applications, interoperability, and backward compatibility
Data Rates | 1.0625 to 56.0 Gbps (NRZ); 32.5 to 112.5 Gbps (PAM4)
Configurations | X1 (2-PLL variants), X4 (4-PLL variants)
AVDD/DVDD Range | 1.2V -19%/+3% / 0.75V -3%/+10%
Temperature Range | -40⁰C to 125⁰C
Power (Typical) | 530 mW/lane at 106 Gbps long reach (1 active PLL/lane)
Area | 1.905 mm2; 1363 µm (W) x 1397 µm (H); 4-port/4-PLL

## Slide 7: COMPHY_112G_ADC
IP of the COMPHY (Common PHY) family for 112G LR application
  Provides an aggressive analog + digital power/area while maintaining top-notch performance
Application: Switch, PHY, ASICs
Main networking standards
    Ethernet: IEEE 802.3ck - PAM4 106.25Gb/s - 100G Backplane (KR) and Cable (CR)
    OIF: Common Electrical I/O (CEI) 112G - Long Reach (LR)
  50G mode: IEEE 802.3cd – PAM4 53.125 Gb/s (+OIF)
  25G mode: IEEE 802.3bj – NRZ 25.78125 Gb/s (+OIF)
  10G mode: IEEE 802.3ap – NRZ 10.315 Gb/s (+OIF)
  Down to 1G speed

## Slide 8: Marvell Backplane Core Offering Matrix
Note:
Support PCIe Gen5 (1a) and PCIe Gen6 (1b)
N5 112G LR 4-Port core 4-PLL with Repeater
N5 112G LR 4-Port core 5-PLL in E/W (3a) and N/S (3b) orientation
Sizes highlighted in RED are currently under development. Other sizes are estimates and will be considered for development if approved by top management
N7 112G LR core development on HOLD
32G core for 4-Port/2-PLL and 1-Port/2-PLL are w/o PIPE (does not support PCIe)
Core | Tech | 1-Port Core | 2-Port Core | 4-Port Core |  | 
 |  | 2-PLL (X/Y) | 2-PLL (X/Y) | 2-PLL (X/Y) | 4-PLL (X/Y) | 5-PLL (X/Y)
64G LR | N7 | 1.10mm x 0.56mm | 1.19mm x 0.79mm | 1.30mm x 1.27mm | 1.205mm x 1.434mm1a | N/A
112G LR | N7 | N/A | N/A | 2.06mm x 1.23mm | 1.74mm x 1.40mm | N/A
32G | N5 | 0.846mm x 0.568mm | 0.87mm x 0.82mm | 0.846mm x 1.287mm | 0.835mm x 1.484mm | N/A
64G LR | N5 | 0.935mm x 0.546mm1a | 0.96mm x 0.79mm | 1.03mm x 1.27mm | 0.935mm x 1.433mm1a 0.989mm x 1.433mm1b | N/A
112G LR | N5 | 1.363mm x 0.534mm | N/A | N/A | 1.363mm x 1.398mm 1.563mm x 1.398mm2 | 1.380mm x 1.290mm3a 1.260mm x 1.610mm3b
112G XSR | N5 | N/A | N/A | 8-Port/1-PLL: 1.492mm x 1.189mm 16-Port/1-PLL: 1.62mm x 2.10mm |  | 

## Slide 9: Core Configurations:
1-port / 2 PLL
4-port / 4 PLL
4-port / 4 PLL (Repeater)
4-port / 5 PLL
Lane3
Lane2
Lane1
Lane0

## Slide 10: Silicon Proven 5nm SerDes IP
112 Gbps SerDes IP
Numerous internal product tape-outs w/ 112G
112G core <1e-9 BER >37 dB channel
~150 fs RJ TT / <200 fs RJ over PVT
112 Gbps Testboard

## Slide 11: 5nm 112G SerDes Performance: Cisco Evaluation
    Cisco measurements:
    Marvell 5nm 112G SerDes
      IL: 40dB @ 1e-8 BER @4.9pJ/bit
  NET – Marvell 112G LR has Industry Leading Performance
Bit Error Rate (BER)
Marvell 112G SerDes
(5nm)
26
1e-10
1e-8
1e-6
1e-4
31
1e-5
1e-7
1e-9
36
41
46
51
Insertion Loss (dB)
BETTER
Competitors
BETTER
Significant margin with respect to IEEE spec

## Slide 12: 5nm 112G SerDes Performance: Google Evaluation

## Slide 13: Top Level Block Diagrams
Quad macro
Shared common blocks
Dedicated PLL for each lane
DAC-based SST driver
High performance AFE
DSP based adaptive RX equalization
PIN_RX
PIN_TX

## Slide 14: Sub-level Blocks Introduction
COMPHY_112G_ADC sub-level blocks
  Tx
  Rx
  PLL
  COMMON

## Slide 15: 5 nm COMPHY_112G_ADC Rx Architecture
Fang Dong
CE AMS Team
11/29/2022

## Slide 16: COMPHY_112G_ADC Rx Overview
High bandwidth and low noise AFE with data rate supporting up to 112.5 Gbps
  CTLE for pre-equalization
  Timing Interleaved (TI) ADC for signal digitization
The Rx DSP in digital domain includes
  A digital data-path for data recovery
  A digital clock-path for clock recovery
  Equalization adaptation engines
  ADC calibration engines
  Metric monitors
FW-based sophisticated training algorithm to optimize the performance across PVT

## Slide 17: Analog vs ADC-Based SerDes:
 |  | ADC-Based | Analog | Comment
Equalization | Equalization capabilities | TX-FIR, CTLE, RX-FFE, DFE (1 tap) | TX-FIR, CTLE, DFE (multiple taps) | Challenges to achieve 1st DFE tap with analog SerDes at higher speeds
 | Precursor Cancellation | TX-FIR, RX-FFE | TX-FIR only | DFE can cancel only post-cursor ISI
 | Modulation Scalability | Easier to scale for higher order modulation | Harder to scale for higher order modulation | Complexity quickly grow with modulation in analog SerDes More DSP can be used in ADC SerDes
Timing Recovery |  | Baud-rate/oversampled higher latency | Bang-bang CDR (edge/data) lower latency | Mueller-Müller as Baud rate timing recovery
Power |  | Competitive in PAM4 Higher power in NRZ | Lower power | Smaller technology nodes improving efficiency of ADC SerDes
Process Sensitivity |  | Less process sensitive | Very sensitive to process | Analog SerDes requires precise calibration across PVT
Scaling |  | DSP portion scales well with technology node | Doesn’t scale well with technology node | Analog porting is re-design for both
Portability |  | Easier to port design | Harder to port design | Focus on digital side

## Slide 18: Rx Block Diagram

## Slide 19: Rx Front-End
Input network bandwidth extension with inductors and t-coil
Variable capacitor for high frequency gain programmability
Impedance calibration
2-stage CTLE provides up to 18 dB peak gain

## Slide 20: COMPHY_112G_ADC – RX CTLE
Continuous Time Linear Equalizer (CTLE)
  2 cascaded equalization stages
  providing 2 zeros and 4 poles

## Slide 21: CTLE Gain Range
Total = 22.2 dB DC gain range
Peak Range = 19.1 dB

## Slide 22: Rx Track and Hold (T/H) ADC
8X8 interleaving
8 T/H sample + BUF
8 SAR per T/H bank
SW7
SAR7
SAR63
Buffer(1X)
A0
A7
From CTLE
SW0
SAR56
SAR0
Buffer(1X)
A0
A7
SW1
SAR1
Buffer(1X)
A0
A7
SAR57

## Slide 23: COMPHY_112G_ADC – TI-ADC
Structure/Resolution/Speed
8x8 Timing Interleaving, balance of complexity and power (64 Sub-ADC)
Programmable - 4~7bit,
Sampling speed - 3.5~56GS/s
Features for optimizing power
Scalable/Adaptive supply
Scalable/Adaptive resolution
Scalable input Dynamic range (Performance control)
Scalable sub-ADC count (8/16/32/64 sub ADC)
Low power SAR with custom logic
Background digital calibration engines
Offset, Gain and Skew calibration in digital domain
Simple, Flexible, Robust

## Slide 24: Rx Digital Block Calibrations
Gain/offset calibration
  Remove the analog gain and offset mismatch of each separate ADC
  Find the optimum gain coefficients which brings the average of the amplitude among different SAR to be equal
  Remove the DC offset of each ADC
Skew calibration
  Compensates the T/H sampling timing skew error
AGC
  Adjust the ADC input dynamic range to fully utilize ADC resolution by reusing the ADC gain calibration target hardware

## Slide 25: Rx Digital Block Calibration Registers
Gain/offset calibration
  rx_adc_if_gain_word{0:63}_lane[5:0]
  rx_adc_if_ofst_word{0:63}_lane[6:0]
Skew calibration
  skew_adapt{0:7}_lane[8:0]
AGC
  rx_adc_if_agc_gain_lane[4:0]
Calibration | Resolution | Range
Offset | ¼ ADC LSb | ±16 LSb
Gain | 1/128 | ±25%
Skew | 50 fs | ±4 ps

## Slide 26: COMPHY_112G_ADC ADC Calibrations
ADC calibration results on Raptor2 GUI

## Slide 27: ADC Configuration Depending on Speed
Speed mode | Sampling rate (GSamp/s) | Clock rate (GHz) | Over-sampling | #THs
112G-PAM4 | 50 - 56 | 12.5 - 14 | None | 8
56G-NRZ |  |  |  | 
56G-PAM4 | 14 - 28 | 7 - 14 | None | 4
28G-NRZ |  |  |  | 
10G (NRZ) | 7 - 14 | 7 - 14 | None | 2
5G (NRZ) | 3.5 - 7 | 7 - 14 | None | 1
3G (NRZ) | 3.5 - 7 | 7 - 14 | x2 | 1
1G (NRZ) | 3.5 - 7 | 7 - 14 | x4 | 1

## Slide 28: Rx Clock Generation
8-bit Phase Interpolator (PI) is driven by the clock recovery loop
8-phase clock for T/H with skew compensation

## Slide 29: RX Analog Calibration
RX impedance calibration (one time calibration)
  Target to 50Ω single end
RX dcc-align90 calibration (continuous calibration)
  Data clock duty cycle correction
  Multi-phase generation calibration
  Data clock phase alignment calibration

## Slide 30: Rx Digital Data Path
Data path equalization
  Feed Forward Equalizer (FFE)
  Decision Feedback Equalizer (DFE)
Data path bus width conversion (gear box)
  Convert analog bus width to SoC bus width
Gear box (not shown in the plot)
The slicer output goes to gear box then to SoC

## Slide 31: Rx Data Path FFE
Provides a linear FIR block to better equalize the channel loss
Process ADC samples to remove pre-cursor and post-cursor ISI
FFE supports 6 pre-taps, 16 post-taps and 8 floating-taps cover up to 120 UI
FFE tap adaptation is achieved with sign-error LMS adaptation engines
This block includes gain and BLW offset compensate logic
M-tap FFE
Speed mode | # FFE precursors | # FFE postcursors | FFE floating taps
112G/56G/28G | 6 | 16 | Yes
10G | 4 | 10 | Yes
5G | 2 | 5 | Yes
3G/1G | 1 | 2 | No
Notes: BLW

## Slide 32: FFE Key Registers
DP FFE key registers
  rx_dp_lms_ffe_pre{6:1}_coe_lane[2:0]
  rx_dp_lms_ffe_pst{1:16}_coe_lane[6:0]
  rx_dp_lms_ffe_flt{1:4}_b0_coe_lane[2:0]
  rx_dp_lms_ffe_flt{1:4}_b1_coe_lane[2:0]
  rx_dp_lms_gain_coe_lane[10:0]
  rx_dp_lms_blw_coe_lane[5:0]

## Slide 33: Rx Data Path DFE
1-tap unrolled DFE
Output symbol level at the slicer are +3, +1, -1, and -3 in PAM4 and +3 and -3 in PAM2
DFE tap adaptation is achieved with LMS adaptation engines
DFE key registers
  rx_dp_lms_dfe_coe_lane[5:0]
Notes: BLW

## Slide 34: Rx Data Path FFE + DFE
ADC output
FFE + DFE
Data path slicer input
time
time
Normalized Unit (+/-1.0)
mid-th
bot-th
top-th
Digital value
Notes: BLW

## Slide 35: Rx Digital Clock Path
DTL-FFE with 6 taps
TED (timing error detector)
Loop filter
Phase integrator

## Slide 36: COMPHY_112G_ADC – RX Clock Path FFE
Provides a Finite Impulse Response (FIR) block to better equalize the channel loss.
This block includes gain and BLW offset compensate logic.
It is a simplified version of data path FFE. The FIR FFE supports 3 pre-tap and 3 post-tap

## Slide 37: Rx Clock Path FFE
Clock path FFE key registers
  rx_dtl_lms_ffe_pre3_coe_lane[3:0]
  rx_dtl_lms_ffe_pre2_coe_lane[4:0]
  rx_dtl_lms_ffe_pre1_coe_lane[5:0]
  rx_dtl_lms_ffe_pst1_coe_lane[5:0]
  rx_dtl_lms_ffe_pst2_coe_lane[4:0]
  rx_dtl_lms_ffe_pst3_coe_lane[3:0]
  rx_dtl_lms_blw_coe_lane[4:0]
  rx_dtl_lms_gain_coe_lane[9:0]

## Slide 38: Rx Clock Recovery
The timing error detector (TED) extracts phase information based on the error and the decision. It is based on a modified version of Mueller-Muller algorithm.
Low-speed TED is based on Bang-Bang phase detector. It is available for speed lower than 14G NRZ
This phase information is inserted in a second order loop filter to generate the frequency adjustment
The phase integrator accumulates the frequency adjustment of the loop filter and provide a new phase update to PI

## Slide 39: Clock Recovery—Mueller-Muller vs. Edge Detector
MM detector (1X)
Single phase RX clock
  Lock to data
  Already on data phase
See all equalization
  TX-FIR + CTLE + FFE-DTL
Requires uncorrelated random data
Edge detector (2X)
2 phases (edge+data) required
  Lock on edge
  Data clock 90˚ apart
See analog equalization
  TX-FIR + CTLE
Requires edge transitions

## Slide 40: Rx Clock Path Key Registers
Loop filter bandwidth settings
  rx_dtl_lpf_kp_shift_lane[3:0]
  rx_dtl_lpf_kp_frac_lane[1:0]
  rx_dtl_lpf_ki_shift_lane[4:0]
  rx_dtl_lpf_ki_frac_lane
DTL clamping settings
  rx_dtl_clamping_en_lane
  dtl_clamp_rst_mode_lane[1:0]
  rx_dtl_clamping_val_lane[6:0]
  dtl_clamping_triggered_lane
  clear_dtl_clamping_triggered_lane
Notes: TED,

## Slide 41: COMPHY_112G_ADC – RX Digital Equalization Monitors
Mean Square Error (MSE) for SNR measure
  (PAM4)
  (PAM2)
Signal monitors collecting statistics of ADC output and other points in digital equalization path
  Average, abs power, histogram
  ADC saturation check, quality check of ADC calibrated output.
On-chip memory (OCM) to dump up to 4K consecutive samples of ADC output and other points in equalization path
  ENOB estimation, proof of concept, debug purpose

## Slide 43: 5 nm COMPHY_112G_ADC PLL Architecture
Eugene Kim
CE AMS Team
11/29/2022

## Slide 44: TL10 TOP
TL10 will have one LCPLL with all register prefix: PLL_CMN_***
LCPLL output cover range: >=12.5G
LCPLL is the same design as conventional 112G products
TL10 will have four Ring PLLs with all register prefix: PLL_TS_*** and PLL_RS_***
Ring PLL cover range: =<12.5G

## Slide 45: PLL Block Diagram
Please use PLL_CMN to replace PLL_TS as prefix for TL10
Notes: TS, RS

## Slide 46: LCVCO Temperature Compensation
VCO has some temperature compensation varactors In order to optimize the performance of the PLL.
Varactors are sequentially made to move from the min to max capacitance
Temperature compensation is accomplished via 11 varactor banks to have glitchless varactor controls
Varactor must be gradually switched from being tied to AVSS to AVDD (or vice versa)

## Slide 47: Temperature Compensation Flow
A series of 2 comparators encode 3 potential levels: vcon_h, vcon_l, and vcon_m can be read from digital logic called TEMPC_LEVEL_TODIG[1:0]’
An intervening 8-bit DAC is originally set to AVSS
DAC is slowly incremented every 40 µs
Total transition from AVSS to AVDD takes 256 × 40 µs = ~10 ms
Digital detects TEMPC_LEVEL_TODIG[1:0]’ every 5 µs (200k). The flow chart shows:
  DAC code increases, the frequency increases
  DAC code decreases, the frequency decreases
Notes: TS, RS

## Slide 48: VCO Coarse Tuning
The Divide by 1.5 mode has a limitation of a maximum of 20.66 Gb/s primarily due to duty cycle and DJ concerns at higher frequencies
The PLL uses and LC-based VCO with a dual mode control on the inductor to tune the inductance slightly by introducing a parasitic loop around the primary coil
The primary coil is shown in green, and the parasitic loop is shown in black
Notes: TS, RS

## Slide 49: VCO Coarse Tuning (cont.)
The low frequency is achieved when the PLL_TS_VIND_BAND_SEL_LANE signal is low.
  This signal drives the gate of the shorting NFET, so when the gate is low, the NFET is off, and the parasitic loop is not enabled
The biasing of the Source/Drain (S/D) of the switch is achieved by setting PLL_TS_VIND_BIAS_EN_LANE = 1
  This turns on the NFET, pulling the S/D of the switch NFET to GND, thereby inducing a channel and completing the parasitic loop.
Notes: TS, RS

## Slide 50
PLL VCO Tuning Range
PLL VCO Frequency Ranges
VCO Range | Frequency
SLOW (Parasitic Loop OFF) | 10.8 – 15.7 GHz
FAST (Parasitic Loop ON) | 11.6 – 17.9 GHz
The default bandwidth is 1 MHz, and the range is 0.5 to 2 MHz

## Slide 51: PLL Calibration
The PLL calibrations—Default bandwidth is 1 MHz, and the range is 0.5 to 2 MHz frequencies, mode amplitude, mode temperature compensation, speed-change, and duty cycle.
  Power up calibration—Calibrates to target frequencies
  Continuous mode amplitude calibration—The VCO output amplitude should be large enough to accommodate this calibration
  Mode temperature compensation calibration—The LC PLL should be always locked over temperature
  Fast start-up or speed change calibration—Fast changes the LC PLL frequency
  Clock duty cycle calibration—Calibrates LC PLL output clock duty cycle to 50%
Notes: TS, RS

## Slide 52: RPLL Structure 1/2
Structure
  PLL
  MUX
  REFBUF
Loop BW
  8 MHz
Lock Range
  6.25 GHz to 12.5 GHz

## Slide 53: RPLL Structure 2/2
Higher accuracy lock detection— Frequency counter
Low jitter—High bandwidth regulator + low jitter VCO
VDDVCO calibration

## Slide 55: 5 nm COMPHY_112G IBIS-AMI Model
Evelina Zhang
CE AMS Team
11/29/2022

## Slide 56: IBIS-AMI Model
IBIS Algorithmic Modeling Interface (IBIS-AMI) is a modeling standard for SerDes PHYs that enables fast, accurate, statistically significant simulation of multi-gigabit serial links
IBIS-AMI models are primarily used to predict a serial link’s performance with an eye diagram and BER
  In a serial link, transmitter and receiver blocks can utilize various types of equalizers including clock and data recovery circuitry
IBIS-AMI = IBIS + AMI

## Slide 57: AMI Model
At high speed with the DFE and FFE, the IBIS model is no longer sufficient to represent the Tx and Rx circuits
An extension to IBIS has been developed known as IBIS-AMI (Algorithmic Modeling Interface)
The IBIS-AMI model enables fast, accurate, statistically significant simulation of multi-gigabit serial links

## Slide 58: AMI Model (cont.)
In an AMI model, this can be effectively represented at the behavioral level utilizing C/C++.
Because AMI models are compiled C++ models, they cannot be reverse engineered and are, therefore, protected
Consequently, semiconductor vendors can control what details of their IP is exposed to the user, allowing them to freely distribute these models for a wide variety of EDA tools

## Slide 59: IBIS-AMI Model Files
IBIS-AMI Tx model files
IBIS-AMI Rx model files

## Slide 60: Tx AMI Model Parameters
Tx AMI model includes a 6-tap Finite Impulse Response (FIR) filter
The FIR filter is programmed by specifying the parameters:
[ffe_0, ffe_1, ffe_2, ffe_3, ffe_4, ffe_5] = [furthest_pre_cursor, …, furthest_post_cursor]

## Slide 61: Tx AMI Model Parameters (cont.)
The position of the cursor-tap is configurable and can either be at the ffe_3 position or the ffe_4 position
Each coefficient is a dimensionless floating-point value
The coefficients can take on any value, but the following hardware constraint is strictly enforced within the AMI model:
  ∑|𝑓𝑓𝑒𝑘| ≤1.05𝑘=0
If the user specifies a set of coefficient values that would cause this constraint to be exceeded, a scale factor is applied uniformly to all coefficients such that:
  ∑|𝑓𝑓𝑒𝑘|=1.05𝑘=0

## Slide 62: Rx AMI Model Parameters
The primary reserved and model-specific parameters of the Rx IBIS-AMI model are:
Contents of the generated file RX_5FF_COMPHY_112G_ADC_R1.0_ rx_eq_done.txt

## Slide 63: IBIS-AMI Model Simulation Setup

## Slide 64: Rx AMI Model Simulation Result

## Slide 65: Rx AMI Model Correlation Report
Tx Correlation report
Test Measurement Set Up
Model files path
Tx correlation result (corners with revision update) Tx amplitude
    Waveforms collected
    Setting of models
    Model simulation waveform results
    Tx FIR (c0-c5)
    Measurement results collected
    Setting of models
    Model simulation results
Summary
Rx Correlation report
Test Measurement Set Up
Model files path and design parameters
Rx correlation result (corners with revision update) Test conditions:
    Digital Rx figures of merit
    Pass/fall EO criteria
    Correlation results (NRZ, PAM4)
    TT corner graphic EO results
Summary

## Slide 66: Rx AMI EO Pass/Fail Criteria
Minimum SNR criteria
Minimum eye width criteria

## Slide 67: Rx AMI EO Pass/Fail Criteria
After simulation, the Rx model writes the steady-state SNR value to the file: RX_5FF_COMPHY_112G_ADC_R1.0_rx_eq_done.txt
If Keysight ADS is used, this file is written by default to the ./data directory of the current workspace
Another location can be specified by modifying the out-dir parameter from the ADS user interface

## Slide 68: Document and Support
Correlation document for both Tx and Rx
COMPHY_112G_IBIS-AMI_Rx_Model_Correlation_Report_5FF http://ipdoc.marvell.com/ceips/ReadSharepointFile.php?href=https://sp.marvell.com/central/hsio/Projects/PHY_IPs/IBIS_AMI_MODEL/COMPHY/5nm/112G/Doc/COMPHY_112G_IBIS-AMI_Rx_Model_Correlation_Report_5FF.pdf
COMPHY_112G_IBIS-AMI_Tx_Model_Correlation_Report_5FF http://ipdoc.marvell.com/ceips/ReadSharepointFile.php?href=https://sp.marvell.com/central/hsio/Projects/PHY_IPs/IBIS_AMI_MODEL/COMPHY/5nm/112G/Doc/COMPHY_112G_IBIS-AMI_Tx_Model_Correlation_Report_5FF.pdf
Application document served as user guidance:
COMPHY_112G_IBIS-AMI_Model_App_Note_5FF ( bundled with model)

## Slide 70
Time | Topic | Presenter
8:00 – 8:10 | Short introduction | All
8:10 – 08:40 | Architecture - TX | Dino Wang
8:40 – 8:55 | Architecture - TX Q&A section | 
8:55 – 09:10 | Break | 
09:10 – 09:30 | Architecture – Digital Function | Remby Taas
09:30 – 09:45 | Architecture – Digital Function Q&A section | 
09:45 – 11:00 | Break | 
11:00 – 11:30 | Architecture - DSP | Hongjie Qian
11:30 - 11:45 | Architecture - DSP Q&A section | 
11:45 –12:00 | Lunch | 
AGENDA

## Slide 71: Legal Statement:
CONFIDENTIAL INFORMATION
  The information contained in this presentation is the confidential and proprietary information of Marvell. You are not permitted to disseminate or use any of the information provided to you in this presentation outside of Marvell.
This material MUST NOT be distributed to customers

## Slide 72: 5 nm COMPHY_112G_ADC Tx Architecture
Dino Wang
CE AMS Team
11/30/2022

## Slide 73
Tx Function Architecture Overview
Tx Function Validation Tests
  Tx FIR/Emphasis
  Tx Amplitude
  Tx Calibration
    Tx DCC/Align90 Calibration
    Tx Impedance Calibration
    Tx VDDR Calibration
  Tx Jitter/Eye diagram
Outline

## Slide 74: COMPHY_112G_ADC—Tx Function
Quarter rate architecture
6-Tap Tx FIR with main tap programmability
SST driver with good linearity and low power
Calibrations for PVT variation
Regulators for high-speed clock path
Low voltage and low power design
Beacon, LFPS, Scan Bypass

## Slide 75: COMPHY_112G_ADC—Tx Function

## Slide 76: Tx FIR
The Tx FIR has up to 6 taps with 3 pre-taps and 2 post-taps
Tx FIR resolution is from 0 to 63, the step size is 1.59%

## Slide 77: Tx FIR/Emphasis
Tx main tap = 58
Tx main tap = 58; Tx post1 tap = -5 (de-emphasis)

## Slide 78: Tx FIR/Emphasis
Tx main tap = 58; Tx pre1 tap = -5 (pre-shoot)

## Slide 79: Tx Amplitude
106G PAM4 2T Clock Pattern

## Slide 80: Tx Amplitude
106G PAM4 40T Long Pattern

## Slide 81
TX DCC/Align90 Calibration
Clock duty cycle with E2C calibration — Duty cycle of the common clock from PLL is calibrated to be 50%
Clock 90-degree alignment calibration (cont.) — Calibrates each phase through 90° delay control to generate evenly spaced phases
Non-delay path clock duty cycle calibration (cont.) — Duty cycle of non-delay path clock after phase generation is calibrated to be 50%
90-degree delay path clock duty cycle calibration (cont.) — Duty cycle of 90° delay path clock after phase generation is calibrated to 50%
Clock duty cycle with post divider calibration (cont.) — Post divider is enabled, duty cycle of the divided-down clock is calibrated to be 50%
Tx Calibration

## Slide 82
TX Impedance Calibration
Tx impedance calibration — Calibrates Tx output impedance to be 50Ω
Tx impedance temperature compensation (cont.) — DAC output would change applied voltage on P/NMOS over temperature change
Tx Calibration

## Slide 83
VDDR calibration for clock path and data path
Tx Calibration
trx_vddr_txdata_cal_result_ext_lane[4:0]
trx_vddr_txdata_cal_result_rd_lane[4:0]
trx_vddr_txclk_cal_result_ext_lane[4:0]
trx_vddr_txclk_cal_result_rd_lane[4:0]

## Slide 84: Tx Jitter/Eye Diagram
Tx Jitter
  EOJ (Even-Odd Jitter), J3u, Jrms
  Compliance test —100G/50G KR, CR, C2M

## Slide 85: Tx Eye Diagram

## Slide 87: 5 nm 112G COMPHY Function
Remby Tass
CE AMS Team
11/30/2022

## Slide 88: COMPHY_112G_ADC PHY Functions
Power control sequence
  PHY initialization
  Rx initialization
  Speed change
  Soft reset
Squelch detection
Isolation mode
Loopback mode
PHY test
ACJTAG test
Scan bypass
Burn in test
PHY latency
  TX latency
  RX latency
Eye Opening Mode (EOM)

## Slide 89: Power Control Sequence
PHY power control sequences include power up/down, speed change, soft reset, and more
SoC controls power control PINs
  PIN_PU*, PIN_RESET_CORE*, and more
PHY MCU handles the power sequence and interact with analog circuit
  Example of power up sequence
  Asserting ANA_PU* after PIN_PU* assertion
  Load speed table
  Trigger calibrations (PLL calibration)
  Asserting PIN_PLL_READY after calibration is done

## Slide 90: Initialization
This IP requires all lanes to be power on during the initial power-on sequence, that is, PIN_PU_PLL, PIN_PU_TX and PIN_PU_RX of 4 lanes must be high during the initial power on
The power-on sequence initiates automatically whenever PIN_RESET transitions from 0x1 to 0x0 and PIN_PU_PLL is 0x0
During the power-on sequence, and before the internal PLL of the PHY is ready, the REFCLK outputs on PIN_TXDCLK and PIN_RXDCLK
PHY Initial Power-on Sequence Timing

## Slide 91: Rx Initialization
Rx initialization is performed with pins PIN_RX_INIT, PIN_RX_INIT_DONE, and PIN_RXP, PIN_RXN
45

## Slide 92: Speed Change Sequence
44

## Slide 93: Speed Change
Data rate can be changed by configuring PIN_PHY_GEN_RX and PIN_PHY_GEN_TX
Set PIN_TXDATA_GRAY_CODE_EN, PIN_TXDATA_PRE_CODE_EN, PIN_RXDATA_GRAY_CODE_EN, and PIN_RXDATA_PRE_CODE_EN based on the pre/gray coding requirement before changing PIN_PHY_GEN_RX and PIN_PHY_GEN_TX
The pins PIN_PLL_READY_TX and PIN_PLL_READY_RX de-assert and then re-assert
43

## Slide 94: Speed Change (cont.)
When valid data appears on Rx, the SoC asserts PIN_RX_INIT to initialize the receiver as directed
The same is true in Wake Up from Slumber mode
The REFCLK on PIN_TXDCLK and PIN_RXDCLK can be disabled by setting PHY register REFCLK_ON_DCLK_DIS_LANE = 0x1
43

## Slide 95: Soft Reset
87

## Slide 96: Soft Reset
87
The soft reset is performed by PIN_RESET_CORE_TX and PIN_RESET_CORE_RX and the status is reflected by PIN_RESET_CORE_ACK_TX and PIN_RESET_CORE_ACK_RX
Unlike normal slumber/wakeup and speed change sequences which do not allow any PHY configuration change, soft reset grants the higher layer the flexibility to change the pin configurations, reference clock sources, and the register programming values for the upcoming data transfer after the reset release

## Slide 97: Squelch Detection

## Slide 98: Squelch Detection
Squelch detection detects PIN_RXP/PIN_RXN
  When PIN_RXP/PIN_RXN changes from z to 0/1, sq_out changes from 1 to 0 after 100 ns
  When PIN_RXP/PIN_RXN changes from 0/1 to z, sq_out changes from 0 to 1 after 100 ns

## Slide 99: Squelch Detection For Long 1/0
AC coupling mode, if PHY PIN_RXP/PIN_RXN receive no toggling 1/0 for 10 µs, the PIN_SQ_DETECTED becomes 0x1 and PIN_SQ_DETECTED_LPF becomes 0x1 after the filter time
The filter time is configurable (10 ns to 10 ms) by register SQ_LPF_LANE[15:0]

## Slide 100: Squelch Detection
SQ glitch filter enabled by register SQ_DEGLITCH_EN_LANE
Glitch width is set by register SQ_DEGLITCH_WIDTH_P_LANE, SQ_DEGLITCH_WIDTH_N_LANE
RXP
z
RXN
SQ
sq_out_deglitch
z
z
z
z
latency
glitch
glitch

## Slide 101: Digital Squelch Detection
At higher data rates/long channels, distinguishing signal or noise detection for SQ is difficult
  Digital SQ detection circuit for more robust estimator of signal energy presence from ADC
Digital SQ detector approximates envelope peak detection
  ADC sample compare against peak amplitude estimate
  Increment (with 32)/decrement (with 1) accumulator according ADC sample comparison to peak amplitude estimate
  Tracks the outer envelope of signal rather than average
  Accumulated envelope amplitude compared against threshold for SQ detection

## Slide 102: Isolation Mode
The PHY isolation mode is used to isolate the PHY from SoC control
  In this mode, most of the PHY pins are invalid
  Certain PHY registers are used to replace the corresponding pins
  Only the analog, power supply, DFT and register access pins are valid
This mode is commonly used for debug purpose, which confirms the issue is inside or outside the PHY
This mode is enabled by programming the register PHY_ISOLATE_MODE to 1

## Slide 103: Isolation Mode Pins

## Slide 104: Loopback
This PHY supports the following loopback mode tests:
  Far-end loopback mode
  Local digital parallel loopback mode
  Local analog serial loopback mode
  External loopback mode

## Slide 105: Loopback Control
Far-end loopback mode
  The far-end PHY sends the test pattern through its Tx pads
  The local PHY receives the test pattern at its Rx pads and forwards the received test pattern from Rx to Tx
  The local PHY then sends the test pattern back to the far-end PHY through its Tx pads

## Slide 106: Loopback Control
Local analog serial loopback mode
  The PHY sends the locally generated test pattern to the internal node of CTLE
  The data is looped back to the analog Rx portion of the internal PHY
  The test controller checks the received data and sets the test pass or fail flag accordingly
  Register set: LOCAL_ANA_TX2RX_LPBK_EN_LANE

## Slide 107: Loopback Control
External loopback mode
  The PHY sends a test pattern to Tx
  The test pattern exits the PHY Tx pads through the AC coupling cable and back to the PHY Rx pads
  The test controller checks the received data and sets the test pass or fail flag accordingly
  This feature is ideal for ATE tests
  No need to set registers

## Slide 108: Loopback Control
Local digital parallel loopback mode (SoC bypass the PHY)
  The SoC sends the data on the input PIN TXDATA directly to PIN_RXDATA, bypassing all internal logic of the PHY
  This mode is only a method to loop the data that has its actual origin at the SoC level
  Register set: LOCAL_DIG_TX2RX_LPBK_EN_LANE

## Slide 109: PHY Test
The PHY test function tests the PHY by using pre-defined test patterns This function contains the following modules:
  Pattern generation and transmission module
  Pattern reception and comparison module

## Slide 110: PHY Test Pattern Selection
78

## Slide 111: ACJTAG Test
Rx ACJTAG detects/recovers low frequency beacon/AC-JTAG signals in AC-coupled connection
  Used to detect connection faults on TX and RX differential pins
  COMPHY must reset before performing this task or else analog registers will not toggle

## Slide 112: ACJTAG Test Steps
After PIN_RESET is released, set the PINs to the expected value
Send patterns (maximum 100 MHz) through PINs listed below:
Input PINs | Output PINs
PIN_RXP0 | PIN_RX_ACJTAG_RXP0
PIN_RXN0 | PIN_RX_ACJTAG_RXN0
PIN_TX_ACJTAG_IN0 | PIN_TXP0
 | PIN_TXN0 (Reversed PIN_TXP0)
PIN Name | Value
PIN_RX_ACJTAG_AC0 | 1'b1
PIN_RX_ACJTAG_EN0 | 1'b1
PIN_RX_ACJTAG_HYST0 | 3'b010
PIN_RX_ACJTAG_DCBIAS0 | 3'b010
PIN_RX_ACJTAG_MODE0 | 1'b1
PIN_TX_ACJTAG_EN0 | 1'b1
PIN_RX_ACJTAG_INITN0 | 1'b0
PIN_RX_ACJTAG_INITP0 | 1'b0

## Slide 113: Scan Bypass
Send/receive scan test patterns bypass the COMPHY through Tx/Rx pins

## Slide 114: Scan Bypass (cont.)
Connect PIN_SCN_CLK and all the PIN_AS_SCN_CLK* to 100 MHz (maximum frequency) clock
After PIN_RESET is released, set:
SoC can send patterns through the PINs listed below while performing scan test through *SI* and *SO* PINs
PIN Name | Value
PIN_SCNTEST | 1’b1
PIN_SCN | 1’b1
PIN_SCN_ISO | 1’b1
Input | Output
PIN_SCN_TXP_DIN0 | PIN_TXP0
PIN_SCN_TXN_DIN0 | PIN_TXN0
PIN_RXP0 | PIN_SCN_RXP_DOUT0
PIN_RXN0 | PIN_SCN_RXN_DOUT0

## Slide 115: Burn-in Test
Can perform MBIST at the same time
Analog sends out PRBS pattern on PIN_TXN/P and receives pattern from PIN_RXN/P
Analog regulator voltage raised by 20% through analog internal control
Analog registers have no clock and will not toggle

## Slide 116: Burn-in Test (cont.)
Digital circuit is isolated from analog circuit during analog burn-in mode
COMPHY must reset before performing this task
Steps:
  After PIN_RESET is released, send reference clock
  Set PIN_BURN_IN_TEST to 1

## Slide 117: Tx Latency
Tx data latency—Measured as the time required for the first parallel data bit to appear on the serial bus
Tx idle latency—When PIN_TX_IDLE = 0x1, PIN_TXP and PIN_TXN are in the idle state

## Slide 118: Rx Latency
Rx data latency—Measured as the time between the last data bit on the serial bus to the parallel data clock

## Slide 119: Repeater Mode
Repeater mode according to Ethernet standard
  Tx data of host PHY aligned to Rx data of line PHY
  Frequency of Tx of host PHY follows the frequency of Rx line PHY
  May have ±100 ppm frequency offset to the refclk

## Slide 120: EOM (Eye Open Measure)
Non-destructive RX Internal eye plot, eye height, eye width
  Additional HW to process digital slicer input at different slicer position than main ADC current slicer position
  PAM4 : Top eye, Middle Eye, Bottom Eye
  PAM2/NRZ : Middle Eye only

## Slide 121: EOM Structure
Separate EOM ADC
Channel estimator calculates channel impulse response
Reconstruction filter calculates slicer input at Δτ phase

## Slide 123: 5 nm 112G COMPHY DSP Training
Hongjie Qian
CE AMS Team
11/30/2022

## Slide 124: TRx Training Outline
4 | Tx Training
 | Tx Feed Forward Equalizer (Tx-FFE) Preset and Shape Training
5 | Troubleshooting
1 | Overview
 | Scope and Metrics
2 | Training Flow
 | Top Level Training Stages/States
3 | Rx Training
 | Analog—Continuous Time Linear Equalizer (CTLE) Training Digital Equalization Control—Clock and Data Recovery (CDR)

## Slide 125: Protocol Support
Supported training protocol:
  IEEE 802.3ck – PAM4 100G/lane
  IEEE 802.3cd – PAM4 50G/lane
  IEEE 802.3bj – NRZ 25G/lane
  IEEE 802.3ap – NRZ 10G/lane
Link Training (LT) features:
  Covers IEEE 802.3 clause 72 (10G/25G), 136 (50G), and 162 (100G)
  SoC handle speed Auto-Negotiation (AN) and IP handles LT

## Slide 126: Overview
After startup at the link speed, the Rx applies equalization and determines the quality of the signal before transitioning to data traffic
Start
Training
Data traffic
SoC Triggered
Return to SoC

## Slide 127: Training Scope
Training space
  Tx-equalization
  Rx-Analog Front End (AFE) equalization-CTLE
  Rx-digital equalization – FEE, DFE
Rx quantifies the quality of the signal by multiple Figure of Merits (FOM)
CTLE
FFE
DFE
ADC
to slicer
etc.
channel
Rx Digital Parallel Processing
Analog Front End
TX

## Slide 128: Training Metrics
Figure of Merits (FOM)
  ADC Dynamic Range (ADC-DR)-- does not require recovered clock
  Frequency content of ADC samples -- does not require recovered clock
  Digital equalization shapes -- require recovered clock and/or recovered data
  Signal to Noise Ratio (SNR) -- requires recovered clock and/or recovered data
FOM(s) are measured using hardware monitors and fed to the integrated microcontroller (MCU)

## Slide 129: Training Metrics ADC-DR
Target ADC-DR—Defined by ADC threshold
  ADC output (input of FFE) range = -64 to +63
Saturation measured by sample count beyond target DR (CDF)
CTLE
FFE
DFE
ADC
slicer
rx_in
Rx Digital Parallel Processing
Analog Front End
dcs

## Slide 130: Training Metrics Frequency Content of ADC
Equalization as measured by frequency content
CTLE
FFE
DFE
ADC
slicer
rx_in
Rx Digital Parallel Processing
Analog Front End
dcs
  ()-> LP filter –> LP content
  ()-> HP filter –> HP content
+
-
LP
HP
LP Content
HP Content
Eq. metric

## Slide 131: Training Metrics SNR and Equalizer Shape
Performance optimization after clock recovery (and/or data recovery) based on SNR and digital equalizer shape
CTLE
FFE
DFE
ADC
slicer
rx_in
Rx Digital Parallel Processing
Analog Front End
+3
-3
+1
-1
SNR
Digital Equalizer

## Slide 132: FOM Monitors
Training algorithm control the monitors and observe FOMs from MCU
channel
CTLE
FFE
ADC
to slicer
etc.
Rx Digital Parallel Processing
Analog Front End
MCU for training algorithm, adaptation control etc.
LMS-FSM
Monitor
select
TX
Via remote request

## Slide 133: Training Flow
FW training controls the training algorithms and state-machine
Tx-training has additional steps
Standard dictates the modulation types and presets for Tx-training

## Slide 134: CTLE Training
2 steps:
  Required param tuning
  Optional param tuning
Setting initial CTLE necessarily does not change the trained CTLE values, rather speed up the training
Decision to tune optional CTLE param is based on saturation or ADC-DR usage
Optional CTLE tuning is only required for very extreme channels (very short or very long)

## Slide 135: CTLE Parameters—R, C, GC
Analog control are mapped to training control for simplification and ease of use
Training controls
  DC gain: R
  Peak gain: C
  Broadband gain: GC
Boost = Peak - DC
Param Increase | DC Gain | Peak Gain | Boost
R |  |  | 
C |  |  | 
GC |  |  | 
Examples at 100G
R
GC
C

## Slide 136: CTLE Training—R, C, GC vs FOMs
ADC-DR impacted by R, C, GC
LP more impacted by R (DC-Gain)
HP more impacted by C (Peak-Gain)
GC (broad-band gain) has similar impact on LP and HP
Saturation count shown in pic, as a % div by total count = 216

## Slide 137: CTLE Training—R, C, GC
R, C, and GC training
Does not require recovered clock
Find the (R, C) which provides good equalization
Find the (R, C, GC) which minimizes saturation and maximizes ADC-DR usage

## Slide 138: Optional CTLE Parameters
Optional training controls—Attenuation
Param Increase | DC Gain | Peak Gain | Boost
A |  |  | 
Examples at 100G
A
A
Saturation count shown in pic, as a % div by total count = 216

## Slide 139: Optional CTLE Param Training—Attenuation
Additional CTLE param training
Only applicable in very short or very long channels
Does not require recovered clock
Find attenuation which minimizes saturation and maximizes ADC-DR usage
Adjustment of R, C, GC necessary

## Slide 140: CTLE Training—Troubleshooting
Is ADC-saturated? Or well below target DR?
  OCM from API/Raptor2 GUI
  Test Point (TP): ADC saturation measure
  The following registers should be at a low value (order of 10s; not 100s)
    rx_train_adc_in_sat_60_at_train_end_lane[15:0] – 94% (60/64) ADC-DR
    rx_train_adc_in_sat_56_at_train_end_lane[15:0] – 87% (56/64) ADC-DR

## Slide 141: CTLE Training—Troubleshooting
Troubleshooting
  CTLE controls
    For a longer channel expect higher gain and boost (higher C, higher GC)
    For shorter channel expect lower gain and boost (lower C, lower GC)
    R usually higher unless very large Tx-FIR pre-emphasis

## Slide 142: CTLE Training—Troubleshooting
Test points
The range quoted here are absolute maximum, and depends on speeds and other CTLE controls
Training usually operate on different ranges depending on speed
CTLE attenuation is expected to be 0 (default) for most channels
Param | Functions | Range (Code) | Range (in dB) at 100Gbps | Comment
rx_train_ctle_C_lane[7:0] | CTLE peaking control | [0, 45/64] | 13 dB at peak [0, 45] at 100G | Finer control, Higher resolution
rx_train_ctle_GC_lane[4:0] | CTLE Broadband gain control | [0, 15] | 11 dB at nyq | Coarser control
rx_train_ctle_R_lane[4:0] | CTLE DC gain control | [0, 15] | 22 dB at DC | Coarser control
rx_train_ctle_atten_lane[7:0] | CTLE attenuation control | [-21, 20] | 11 dB at nyq [-9 to 18] at 100G | Coarser control

## Slide 143: Clock and Data Recovery (CDR)
Hardware loops, training only controls
  Enables
  Related parameters
Important for troubleshooting
Clock recovery achieved with a dedicated digital path performing a local data recovery and timing error estimation—clock path/digital timing loop
Data recovery is achieved with a dedicated digital path with recovered clock from clock recovery—data path
Data-path equipped with longer FFE and an DFE

## Slide 144: Clock Recovery
In higher speed, Rx clock recovery is done by a Mueller-Muller detector which feeds a second order loop driving the Rx clock generation
Training controls the enables and related parameters of different loops
Training controls the LMS engine of DTL-FFE
Parameter | Spec
FFE pre-cursor # | 3
FFE post-cursor # | 3

## Slide 145: Data Recovery
Training controls the enables and related parameters of different loops
Training controls the LMS engine of DP-FFE, DFE
FW-based training optimize
  Position of floating banks
  Number of active taps
Parameter | Spec
FFE pre-cursor # | 6
FFE (fixed) post-cursor # | 16
FFE floating # | 2 banks of 4 taps up to 120 UI
DFE # | 1

## Slide 146: CDR Troubleshooting
DTL Clamping—Frequency offset exceeded pre-defined range (±500 ppm)
  dtl_clamping_triggered_lane
Frequency offset should not be very large
  From Raptor2 GUI
  From registers
    Toggle rx_dtl_fofst_req_lane
    Read rx_dtl_fofst_stable_lane[31:0]—In ppm: rx_dtl_fofst_stable_lane[31:0] x 1e6 /2^41.0

## Slide 147: CDR Troubleshooting (cont.)
Tp-SNR (divide by 2^5, add +7 for PAM4, +9 PAM2 to get SNR in dB)
  Clock path
    trx_tp_snr_dtl_bf_train_end_lane[15:0]
    trx_tp_snr_dtl_af_train_end_lane[15:0]
  Data path
    trx_tp_snr_dp_bf_train_end_lane[15:0]
    trx_tp_snr_dp_af_train_end_lane[15:0]
  During mission mode—[read SNR in (mil) dB]
    Read SNR via API
    Read SNR via Raptor2 GUI

## Slide 148: CDR Troubleshooting (cont.)
Digital equalizer shape
  No hard and fast rules
  — Is there any saturated taps?
  Registers —Toggle rx_eq_rd_req_lane to read
    For CP/DTL
      For filter coefficents – read rx_dtl_lms_ffe_*_coe_lane[x:0]
      For gain – read rx_dtl_lms_gain_coe_lane[9:0]
      For blw – read rx_dtl_lms_blw_coe_lane[4:0]
    For DP
      For filter coefficents – rx_dp_lms_ffe_*_coe_lane[x:0], rx_dp_lms_dfe_coe_lane[5:0]
      For gain – read rx_dp_lms_gain_coe_lane[10:0]
      For blw – read rx_dp_lms_blw_coe_lane[5:0]
How to tell a tap is saturated
  Filter coefficients are signed
  For bit-width of X → tap range -2^(X-1) to +2^(X-1)-1
    DTL example: rx_dtl_lms_ffe_pre1_coe_lane[5:0]
      Bit-width = 6 bit; range = -32 to 31
    DP example: rx_dp_lms_ffe_pre1_coe_lane[6:0]
      Bit-width = 7 bit; range = -64 to 63

## Slide 149: Tx Training Algorithm
Algorithm flow implemented in FW
Tx training HW interface is initiated and used to ask for modulation, preset, and coefficient updates
In most channels, in ADC-based SerDes, performance dependence on Tx FIR shape will be much lower due to available pre-cursor in Rx FFE

## Slide 150: Tx Training Preset Request
Initial preset-request is done by checking ADC frequency content
Preset change may unlock CDR
Change in preset requires changes in CTLE (and relock if necessary)
External preset forcing available
  Set trx_train_txffe_preset_ext_en_lane = 1
  Set trx_train_txffe_preset_ext_lane[2:0]
Tx-FIR with no pre-emphasis can cover most channels

## Slide 151: Tx Training Optional Tx FIR Tune
Rx-digital equalization shape and/or SNR considered when requesting remote Tx-FIR coefficient update
Care taken to change remote Tx-FIR gradually and not to unlock CDR

## Slide 152: Training Troubleshooting
Previously discussed
  CTLE troubleshooting
  CDR troubleshooting
Calibration
  ADC Calibration–gain and offset–should be close to center (within 10 code of 0 for most channels)
    Available in Raptor2 GUI
    Registers
      Toggle rx_adc_if_rd_req_lane
      For gain cal - read rx_adc_if_gain_word*_lane[5:0] → only +ve
      For offset cal - read rx_adc_if_ofst_word*_lane[6:0] → can be +ve and –ve
  Skew-calibration should be within reasonable value around center code (138), and should not be close to max (=255) or min (=0)
    Available in Raptor2 GUI
    Registers
      Toggle rx_skew_rd_req_lane
      Read skew_adapt*_lane[8:0]

## Slide 153: Training Troubleshooting (cont.)
Signal detection/Squelch
  PIN_RX_SQ_OUT_LPF_RD_LANE = 1 indicates no signal
    train_abort_reason_lane[1:0] = 3 indicated training aborted due to no-input/squelch
Timeout (important for Tx training)
  TRX_TRAIN_TIMEOUT_LANE = 1 indicates timeout was triggered
    train_abort_reason_lane[1:0] = 1 indicated training aborted due to timeout
PLL lock—Not training related, only troubleshooting
  ana_pll_*_lock_rd_lane = 0 indicates PLL is unlocked
    Lock detection register to check (depends on PLL configuration)
SoC interrupt
- train_abort_reason_lane[1:0] = 2 indicated training was aborted due to interrupt from SoC

## Slide 155
Time | Topic | Presenter
8:00 – 8:10 | Get to know the team | All
8:10 – 8:40 | Firmware | Minh Tran
08:40 – 08:50 | Firmware Q&A section | 
08:50 – 09:05 | Break | 
09:05 – 09:35 | MCESD-API Software | Fang Dong
09:35 – 09:45 | MCESD/API Software Q&A section | 
09:45 – 10:00 | Break | 
10:00 – 10:30 | AE Guideline | Jian Wang
10:30 - 10:45 | AE Guideline Q&A section | 
10:45 – 11:00 | Break | 
AGENDA

## Slide 156: Legal Statement:
CONFIDENTIAL INFORMATION
  The information contained in this presentation is the confidential and proprietary information of Marvell. You are not permitted to disseminate or use any of the information provided to you in this presentation outside of Marvell.
This material MUST NOT be distributed to customers

## Slide 157: Firmware Training Introduction
Minh Tran
CE AMS Team
12/1/2022

## Slide 158: FW Training Outline
3 | COMPHY_112G FW
 | Overall Flow Supported Features Architecture Debug Features Test and Validation
1 | MCU Integration
 | Overall Architecture HW Register Access SW Defined Registers
2 | FW Responsibility
 | Interface to SoC FW-based Features

## Slide 159: MCU Integration: Overall Architecture
Common MCU (CMN MCU)
  Managing common resources
    Temperature Sensor
    Process Monitor
    Common digital circuit
Lane MCU (LANE MCU)
  Managing lane specific resources
    TX/RX
    PLL
    Lane specific digital circuit
Same FW binaries running on CMN/LANE MCU
  Total 128K with 4 32K banks
MCU 0
MCU 1
MCU 2
MCU 3
CMN Block
MCU CMN
Lane 0
Lane 1
Lane 2
Lane 3

## Slide 160: MCU Integration HW Register Access
All HW are used as memory mapped device
  HW are mapped to external memory space of MCU
  A bus with arbiter is responsible for handling MCU’s external memory request

## Slide 161: MCU Integration FW Defined Registers
Additional memory blocks added to the PHY
  XDAT_CMN
    Memory block can be accessed by all MCUs
  XDAT_LANE
    Memory blocks can only be access by the MCU of that lane
Access control is similar to HW registers
Used to defined register with flexibility (especially in post-silicon)
  Additional FW control (XXX_CAL_EXT_EN)

## Slide 162: FW Responsibility—Interface to SoC
FW acts as the interface between SoC and the PHYs HW circuit
SoC communicate with PHY though PINs
FW read PINs to take necessary actions to make PHY into an expected condition

## Slide 163: FW Responsibility—FW-based Features
Enhance PHY functionality
  Add more PHY features after tapeout
  Add More flexible PHY configuration and routines
  Implement workarounds for corner cases and HW issues
Enhance PHY flexibility
  Add features to support degugging control of configurations and routines
  Allow easy trial-and-error with quick turns on different PHY settings

## Slide 164: FW Overall Flow
Init power up consists of:
  Power up
  PHY configuration
    Speed dependent
    AVDD dependent
    Temp dependent
    PLL usage dependent
  Calibrations
FW polls necessary PINs and register in the scheduler to decide what to do next
  Power down/up, soft reset, data rate change
  Training
  Extra features
    CLI mode
    Severe SNR indication
    Etc.
Power up
PHY configuration
Calibration
Scheduler
Power down
Training
Extra Features

## Slide 165: FW Architecture
Hardware Driver API
Hardware Drivers
SerDes Hardware
Firmware Modules
Top-Level Firmware

## Slide 166: FW Architecture
SerDes Hardware
Top-Level Firmware
Driver API
Digital Drivers Analog Drivers MCU Drivers MISC. Drivers
Powerup & Reset
Power Management
Calibration
CMD IF
Speed Change
Training

## Slide 167: COMPHY_112G_ADC FW: Supported Features
Independent Tx, Rx Power Management for SERDES Mode
Calibration
Independent Tx, Rx Speed change for SERDES Mode
TRX Training
Real Time CTLE tracking
Real Time Phase Adaptation
EOM
CLI Mode
Access Point
Supports Multiple Rx/Tx PLL sharing Configurations

## Slide 168: FW Command Line Interface (CLI) Mode
Register commonly used functions/routines in CLI
Directly execute these routines with simple register access
  CLI_ARGS
  CLI_CMD
  CLI_START
  CLI_RETURN

## Slide 169: FW Debug Feature—Access Point (AP)
AP is predefined in FW
FW can be paused and resumed during execution on the bench by specifying the AP number during power on
Inspect FW routines step by step
Override configurations for calibration/training
Largely decreased number of debug FW used on post-silicon debugging

## Slide 170: COMPHY_112G_ADC FW: FW Test and Validation
Pre-silicon Simulation Regression
Traditional Tests
reg and pin w/r verification.
test data link loopback
Dump analog default value matching
Digital/analog interface validation tx_train_if auto train
tx_train_if link_train_mode Tx train PRBS check
Tx train PRBS check
tx_train_if normal,TRX_TRAIN_SPEED_UP tx_train_if link train,TRX_TRAIN_SPEED_UP tx_train_if BYPASS_TRAIN
_SOC_SPECIFIC_MEM
APB Write/Read pram test SIF Write/Read pram test
APB3 writes and read 2K commom xdata
SIF writes and read 2K commom xdata APB3 writes and read 2K lane xdata SIF writes and read 2K lane xdata DTX
LC PLL without init_freq_offset LC PLL with init_freq_offset
LC PLL with init_freq_offset and ssc DTL
PM CTRL
speed change PLL calibration
DTX frequency loop test cases Repeat Mode Diff Rate
DFE intg/inf
Couple mode scan and jtag
Daily Regression on >500 Test Cases
Automated Daily Regressions
  Runs When Check-Ins Detected for the Day
  Daily Results Sent to Subscribers
Regression Test Categories:
  Register, PIN W/R
  Digital/Analog Interfaces
  Training Interfaces
  APB/SIF Interfaces
  APB/SIF Memory W/R
  DTX, DTL, PLL Validation
  Speed Changes
  Calibrations
  DFE Integrator and Interface
  Coupling Mode
  Scan and Jtag

## Slide 171: COMPHY_112G_ADC FW: FW Test and Validation
Post-silicon Bench Regression
FW Release Regressions
  Runs Before release a new official FW
  Automated Report Generation & Email Notification
  Include Calibration and Training Test
Regression Test Categories:
  Performance (BER)
  Calibrations
  Speed Changes
  TRx Training
  Power management

## Slide 173: 5 nm COMPHY_112G MCESD/API
Fang Dong
CE AMS Team
12/1/2022

## Slide 174: Supported CE SerDes IPs
Fully Implemented
Upcoming
12 nm COMPHY_12G_PIPE4_1P2V R2.0
12 nm COMPHY_28G_PIPE4_RPLL_1P2V R1.0
12 nm COMPHY_112G_X4 R1.x
5 nm COMPHY_32G_PIPE5_X4_4PLL R1.0
5 nm COMPHY_56G_PIPE5_X4_4PLL R1.x
5 nm COMPHY_56G_PIPE5_X1_2PLL R1.0
5 nm COMPHY_112G_ADC_X4_8PLL R1.x
5 nm COMPHY_112G_ADC_X4_4PLL R1.0
5 nm COMPHY_112G_ADC_X4_5PLL R1.0
5 nm COMPHY_64G_PIPE6_X4_4PLL R1.0

## Slide 175: CE SerDes Driver (API)
Notes: Users can integrate the driver into their own applications. This is an overview of how various user applications would call MCESD API functions.
The users' application in blue integrates the MCESD API for a specific IP. The MCESD API uses the callbacks the application provides. These are responsible for accessing the IP in the SoC.

## Slide 176: Getting Started with MCESD
Requirements
Initializing the Driver
Read register function
Write register function
Get pin config function
Set pin config function
Wait function
MCESD_STATUS mcesdLoadDriver
(
IN MCESD_U8 ipMajorRev,
IN MCESD_U8 ipMinorRev,
IN FMCESD_READ_REG readReg,
IN FMCESD_WRITE_REG writeReg,
IN FMCESD_SET_PIN_CFG setPinCfg,
IN FMCESD_GET_PIN_CFG getPinCfg,
IN FMCESD_WAIT_FUNC waitFunc,
IN MCESD_PVOID appData,
OUT MCESD_DEV_PTR devPtr
);

## Slide 177: CE SerDes Driver Functionality
Tx Configuration Settings
Rx Configuration Settings
Tx/Rx Training
Tx speed
Tx equalization
Tx polarity
Tx power
Tx PLL
Tx output,
Tx swizzle
Approximately 18 functions
Rx speed
Phase align
CDR
DFE
CTLE
SNR
Squelch detector
Rx polarity
Rx power
Rx PLL
Rx swizzle
Approximately 20 functions
Approximately 4 functions

## Slide 178: CE SerDes Driver Functionality (cont.)
MCU Configuration
Eye Opening Measurement
Other Test Features
FW download
FW version
Lane power
Broadcast
Approximately 9 functions
Initialization
Measurement
Statistics
Approximately 5 functions
Pattern comparator and generator
Temperature sensor
Error injection
Approximately 7 functions
Direct IP Access
IP registers
Register fields
Pin configuration
Approximately 10 functions

## Slide 179: Highlight IP Feature—PHY Test
Configure the data path API_N5C112GX4_SetDataPath(…);
Configure the pattern generator API_N5C112GX4_SetTxRxPattern(…);
Start PHY Test API_N5C112GX4_StartPhyTest(…);
Get comparator statistics API_N5C112GX4_GetComparatorStats(…);
Stop PHY test API_N5C112GX4_StopPhyTest(…);
Notes: This test block can be used to transmit and receive patterns.
The general sequence is to configure data path, pattern generator, start phy test, get comparator statistics and stop phy test.

## Slide 180: Highlight IP Feature—PHY Test Example
Notes: Example code to set up External loopback mode, then configures transmit and receive pattern to PRBS. Starts PHY Test.
Waits 2 seconds to accumulate statistics. Retrieves PHY Test statistics. And finally stops PHY Test.

## Slide 181: New Functions Example for TL10 Project
API_N5C112GX45PLL_DisplayTrainingLog
Retrieves the link training log for an individual SerDes lane
API_N5C112GX45PLL_SetTrainingLimits
Configure Tx FIR, CTLE etc. minimum or maximum values.
API_N5C112GX45PLL_xxx
Record the signal input (like in scope) for further data analysis
Override the default FW PMD per mode
1. NRZ - Receiver to request PRESET or INIT
2. PAM4 - Receiver to request PRESET1 / PRESET2 / PRESET3
3. Gray-Code enable/disable
4. RX Precoding enable/disable
5. Swizzle (MSB-LSB)
6. KR training polynomial identifier 0/1/2/3

## Slide 182: MCESD API Driver Schedule for TL10 Project
January 31, 2023
  Existing API functions from the COMPHY_112G_ADC_X4_4PLL will be implemented on COMPHY_112G_ADC_X4_5PLL
March 17, 2023
  Full API functions ready

## Slide 183: Where to find MCESD
Location http://ipdoc.marvell.com/ceips/util/mcesd.php
  MCESD_X_X_X.zip
  mcesdAPI Release Notes.txt
MCESD_X_X_X.zip
  API
    Source code
  MCESDDocumentation
  Example Python Wrappers
Notes: MCESD can be downloaded from ipdoc.marvell.com

## Slide 185: Validation Test AE Guideline
Jian Wang
CE AMS Team
12/1/2022

## Slide 186: Outline
3 | Compliance Test Example
 | 100G KR Tx Compliance 100G KR Rx Compliance CR Steady State/Linear Fit Pulse Peak Ratio
1 | Test GUI Introduction
2 | Validation Test
 | Characterization Test Compliance Test Regression Test System QA
3 | Validation Test Example
 | TsPI Coupling to RSPLL Issue PLL TempC Optimization

## Slide 187: Raptor2 GUI

## Slide 188: Validation Test by Raptor2 (1)
Dual-Die Board: 4x 112G PHY
  Die0: D0P0 PHY and D0P1 PHY
  Die1: D1P0 PHY and D1P! PHY
Single-Die Board: 2x 112G PHY;
  Die0: D0P0 PHY and D0P1 PHY
Shared PLL mode: 2PLLs used for 4 Lanes
  Lane0/1 share TsPLL or RsPLL
  Lane2/3 share TsPLL or RsPLL
X4 PLL mode: 4PLLs used for 4 Lanes.
  Default: :Lane0: TsPLL; Lane1: RsPLL; Lane2: TsPLL; Lane3: RsPLL
Loading Init file and FW
Broadcast Control
FW version
Tj reading
PLL_lock reading
Reference Clock
Data Rate
1
2
3
4
5
6

## Slide 189: Validation Test by Raptor2 (2)
Rx train only
SNR shown after Rx train
Rx freq offset shown after Rx train
Calibrations.
FEC
Single Bit response
ED: Rx BER reading
1
2
3
4
5
6
7

## Slide 190: Validation Test by Raptor2 (3)
Tx FFE (Tx FIR)
Bus Width setting (160bits/128bits for 106.25Gbs)
CDR settings
Rx CTLE
Rx EOM (NA for this version)
Rx OCM

## Slide 191: Validation Test by Raptor2 (4)
Notes: BER/SNR over time

## Slide 192: Regression Test

## Slide 193: PHY IP Calibration Regression
Data Rate (G) | Data Rate | ADC Calibration | Calibration
SerDes | 112.5 | — | Yes
 | 106.25 | Yes | Yes
 | 56 | — | 100
 | 53 | 100 | 100
 | 28.125 | 100 | 100
 | 25 | 100 | 100
 | 10 |  | 
 | 6.25 |  | 
 | 3.125 |  | 
 | 2.4576 |  | 
 | 1.25 |  | 
Bench test to verify Firmware functionality for each release version from the very early stage.
Two Boards set up to communicate.

## Slide 194: 5nm 112G PHY IP Training Regression
Data Rate |  | FW RX Train | Comparison w/ Python train
SERDES | 112.5G | Yes | 
 | 106.25G | Yes | Yes
 | 53G | Yes | 
 | 25G | Yes | 
 | 10G | Yes | 

## Slide 195: Validation Test

## Slide 196: Validation Flow for Silicon Test of SerDes IP
Hardware
FW Regression Test
Compliance Test
ESD Test
Compliance PVT
HTOL Test
Application Enhancement Test
Validation Reports
Software
Firmware
Bring up Initial Test
Typical Char Test
PVT Char Test
Init Sequence
Compliance Reports
Issue Summary
Errata List
Debugging Issues through JIRA
Performance Tuning and Training Optimization (PTT)
Continue Sys-QA
ESD/HTOL Reports

## Slide 197: Validation Test Items
PLL
Tx
General
Jitter of clock pattern
PLL locking range
PLL crosstalk
Phase noise
Jitter transfer function
PLL temperature compensation
etc
Jitter of PRBS pattern
Amplitude control
Eye-diagram
Duty-cycle control
FIR
etc
Tx/Rx return loss
Timing budget
Power up calibrations
Analog test points
Repeater mode
ACJTAG
etcre
Rx
SQ
Rx interconnection change test
Performance test over channels
Performance over temperature ramping
etc more

## Slide 198: Example 1
RsPLL not locked after power up at NVNT conditions
Issue phenomena
  53.125G/106.25G mode using 4PLL, Lane 0/Lane 2 use TSPLL, Lane 1/Lane 3 RSPLL
  Lane 3 which uses RSPLL randomly shows unlock when 4 lanes are all ON
  Lane 1 has very few chances to fail
  Lane which uses RSPLL will randomly show BER failure from time to time
  When Lane 2 is disabled, PLL of lane 3 will be stable and locked

## Slide 199: Root Cause analysis
112G 3.0 PLL_TS_DTX_CLK will couple PLL_RS_DIG_REF_CLK ;
Disable TSPLL PI, RSPLL Digital side REFCLK will be clean
TSPLL PI enabled, RSPLL REFCLK to digital waveform
FW WA
RsPLL TempC handled by FW.
FW needs to save PLL calibrations after power up.
Side Effects
Only limited data rates supported in FW.
SERDES 12 Data Rates required by PHY BU.
1.25Gbs/3.125Gbs/5.15625Gbs/10.3125Gbs/12.891Gbs/20.625Gbs/25.78125Gbs/26.5625Gbs/53/125Gbs/106.25Gbs/27.95Gbs/90Gbs

## Slide 200: Example 2
Temperature Ramping test setup with 3 DUT (FF/SS/TT)
Issue 1—Temperature ramping testing time too long
Issue 2—Limited temperature units available in the lab
Solution:
Temperature ramping with 3 boards at a time
1 temperature unit covers all 3 corners (1 TT/1 SS/1 FF)

## Slide 201: Compliance Test

## Slide 202: Compliance Coverage
Corners tested
  3 parts from TT, FF, SS at 3 voltage corners over 3 temperature corners (slewed)
  1 lane per corner, multiple lanes per test
All Tx items
  Return loss
  Output waveforms
  Common-mode voltage
  Jitter
Rx items
  All ITOL channels
  All JTOL channels
Standard coverages
  KR: 25G, 50G, 100G
  CR: 10G, 25G, 50G, 100G
  C2M: 50G, 100G

## Slide 203: Example 1—Tx Compliance Test 100G KR
Voltage: LV/NV/HV
Corner Case: FF/TT/SS
Temperature: Tj -40°C/+125°C
Temperature ramping: >10°C/min
Keysight sampling scope N1000A
IEEE 802.3CK application
100G KR/CR/C2M using Keysight sampling scope N1000A
IEEE 802.3CK application

## Slide 204: Example 2—Rx Compliance Test 100G CR
Voltage: LV/NV/HV
Corner case: FF/TT/SS
Temperature: Tj -40°C/+125°C
Temperature ramping: >10°C/min

## Slide 205: Example 3: Tx Compliance Test : 100G CR
Keysight Sampling scope N1000A
IEEE 802.3CK Application
Steady state and Linear fit pulse peak Ratio require Tx no equalization which Tx eye closed.
Test Configuration needs to be changed per Keysight.

## Slide 206: Test Coverage Enhancement

## Slide 207: STC05-R3 Test Configuration Setup on Diamond-Peak1
TR70 Breakout
T
R
112G
64G
112G
64G
DUT Board
Source Board
Janus
cables
Controller
T
R
R
T
T
R
ISI Board
T
R
R
T
R
T
STC5R3
Thermal Head
Bridge Board
STC5R3
Bridge Board
Self Loopback
R
T

## Slide 208: Diamond-Peak1 Test Setup for COMPHY_112G Corner DUTs
FF/SS/TT corners setup
Short trace board and Yukon-1 trace board
Temperature control unit would be set up later

## Slide 209: Yukon-1 Trace Board
The target of the total channel loss (ball to ball) is 10 dB to 35 dB

## Slide 210: Rx Performance Test on OSFP/QSFP COMPHY_112G Cables
FF/SS/TT corners
2-meter cable
Temperature control unit
Rx performance with temperature ramping test